MAKEROM.DOC     CP/M 3.0 on the Commodore 128     28May87

To create the ROM BIOS used by  CP/M  on the  Commodore 128  follow the
procedure listed below.  You will need a 1571 or 1581 disk drive,  or a
1750 RAM disk, for this task.  If you do not have one of these devices,
you will have to make modifications to suit your system.  Slightly more
than a 200K space is needed for the procedure described.

1.  Create a work diskette by using the FORMAT  utility.  If  you  are
    using a 1571 drive select the C128 double sided option. If you are
    using a 1750 RAMdisk (drive M:), make sure it is empty.

2.  Copy the following files to your work disk, using the PIP utility:

        From USER 0:   PIP.COM
                       MAC.COM
                       SUBMIT.COM

        From USER 2:   CXROM.SUB
                       CXROM1.ASM
                       CXROM02.ASM
                       CXROM80.ASM
                       CXROMINT.ASM
                       CXROMK.ASM
                       CPM3.LIB
                       CXEQU.LIB
                       X6502.LIB
                       Z80.LIB

3.  To assemble new ROM code,  select  the  drive  which contains your
    work disk (eg, A:)  and enter:  'SUBMIT CXROM'  and the  automatic
    process will begin.  The output is in the file CXROM.HEX.

4.  This code should be regarded as an invariant portion of  CP/M  for
    the Commodore 128,  and  is  available as source for informational
    purposes only.  For alternatives  to  the  'ROM Loader',  see  the
    source for the FORMAT utility (to support the 1581 disk drive, it
    was necessary to place a new Loader on the 1581 system track).